## Slide 1: Technical Presentation Team SpaceRacer
Audi Autonomous Driving Cup 2016

## Slide 2: Agenda
Architecture
Vision System
Path Planner
Pose Controller
Parking
Demo

## Slide 3: Architecture
Camera
Odometry
Controller
Image Processing
Path Planner
Jury Module
Marker Detection
Keyboard
Pose
RGB
RGB
Road Signs
Lanes
Crossings
Poses
Maneuvers
Maneuvers
Poses
Steering
Speed

## Slide 4: Vision system
Asus Xtion
RGB Image
Preprocessing
Inverse Perspective Mapping
Feature Detection
Lane Data
Crossings
Filtering
Parking spots

## Slide 5: Image Processing Filter
Calculate IPM and Top Down -> World transforms
  From camera angle and position
  From odometry
Manage worker threads
  Spawn and destroy
  Distribute work
Manage preferences and pin connections
  Forward preferences to workers
  Communicate with other filters

## Slide 6: Worker Threads
Configurable number of workers
Staggered execution
Perform IPM
Perform Filtering
  Threshold, Dilation
Perform Feature Detection
  Lanes
  Crossings
  Beginning of parking spaces
Thread 1 | Thread 2
Processing Frame 1 | Idle
 | Processing Frame 2
Idle | 
Processing Frame 3 | 
 | Idle
 | Process Frame 4

## Slide 7: Lane Detection
Data fusion:
Previous lane data
Detected points in filtered image
Extrapolation from found points
Transformed to world coordinates
Center lane:
Contour detection
Known shape, tracked across frames
Filtered using previous data
Matched to expected line
Transformed to world coordinates

## Slide 8: Crossing Detection
Detect corners
Find center point
Find available exits
Calculate goal poses
Find right angles in contour hulls
Check side lengths
Distance known from specs
Angle known from corner sides
Check for free space ahead and to left and right
Relative to center point
Offsets known
Filter out false positives
Check position relative to lanes
Transformed to world coordinates

## Slide 9: Path Planner

## Slide 10: Path Planner Filter
Lane Data
State machine for maneuver execution
Controller Commands
Crossing Data
Odometry
Maneuvers
Triggers to activate/reset other filters
Lights
Data fusion
Road signs

## Slide 11: Path Planner Filter
Generate driving path via data fusion
  Weighted average between:
  Previous driving path
  Right, left and center lane data from worker threads
  Extrapolated points
Merge crossing and road sign data
  Average center points
  Store detection counters
Pose
Path
Lanes

## Slide 12: Pose Controller
Process Block Pose
PI controller
Process Block Velocity
PI controller
Velocity
Steering
Actual pose
Desired pose
t
Pose <x, y, , speed>

## Slide 15: Pose Controller: Results
Steady state error on pose following:
-> Integrator on correction angle

## Slide 16: Parking

## Slide 17: Parking Finder
Detect Parking Area sign
Search for start of parking slots
Approach start of parking slots
Search empty parking slot with ultrasonics
Execute composite maneuver

## Slide 18: Parking Maneuver
Initial starting pose – reference pose
Reorient for entry at 15 degrees from reference
Change orientation to 45 while going backwards
Fix orientation and center car in parking space
1
2
4
3
Reference Pose

## Slide 19: Demo

## Slide 20: Formation Driving
Use cases
  Traffic jams
  Convoys
Implementation
  Leader position extracted from marker
  Follower tracks leader’s path using the pose controller

## Slide 21: Thank you for your attention
Questions?